## Slide 1: Supervised learning for Non Linear Corrections in the LHC
Alejandro Börjesson Carazo
20/11/2023

## Slide 2: Summary
  Introduction
    Theoretical Background
    Methods
  Results
    Correlation study of the LHC resonances
    RDT Feature selection
    Data generation and training
    Response matrix vs ML corrections
  Conclusion and future improvements
  Backup slides

## Slide 3: Introduction
Recap of the work done thus far in ML for non linear optics
Setting up MADNG simulation for RDT tracking and testing bayesian optimization techniques. Testing against PTC. Bayesian optimization scales poorly with number of correctors, so for this case is not a straight forward technique to apply.
Researching the possibilities of using supervised learning techniques is a simpler technique and can be used in the future for more complicated methods
Model creation, error generation
Finding relevant RDTs to predict errors in the triplets (Feature selection)

## Slide 4: Theoretical Background: Bayesian Optimization
Bayesian optimization is a sequential design strategy for global optimization of black-box functions with as few iterations as possible
  For cheap functions to compute, a grid search approach might be possible
  Bayesian optimization uses Bayes theorem to iteratively update our knowledge of the objective function
  Approximation of the ground truth function with a surrogate function, usually Gaussian process
  Finding next sample point with an acquisition function for example expected improvement function, this function quantifies how good each point is as a guess
  Exploration Exploitation hyperparameters help us tune the algorithm!
[1] Fig 1. Bayesian optimization

## Slide 5: Theoretical Background: Supervised Learning
Supervised learning is a type of ML that uses labelled data to improve
  As shown in Elenas paper and in my previous presentation linear errors can be predicted using ML, and linear models perform best
  The idea is to apply the same method to predict non linear errors using non linear optic parameters, RDTs
  There are multiple models that allow for non linear modelling such as neural networks
  In progress
[2] Fig 2. Data pipeline for linear errors

## Slide 6: Methods: Simulation requirements for ML
In order to create a useful ML model, good data is the most important requirement
Meaningful observables, in this case RDTs
High volumes of data! => Fast simulations
Realistic and unbiased …
Tracking + OMC analysis: Too slow
MADX-PTC: Too slow
MADNG: Fast!

## Slide 7: Methods: MADX-PTC Error Simulation
Generate random errors according to WISE table distribution variances
  EFCOMP function to assign the errors in MADX
  Assign relative errors with respect to the quadrupolar strength of the triplet magnets
  So far only testing with normal sextupolar errors, planning on simulating octupolar order errors and skew errors too
  Typo in MADX manual

## Slide 8: Methods: MADNG Error Simulation
Assigning the same errors in MADNG 0.9.7-pre
  Elements have a dknl and dksl attribute
  Applying the same formula as in MADX documentation and multiplying by element length the same KNL errors are obtained
  PYMADNG Was also used since it provides an easy to use python API
  Using the “trkrdt” method in MADNG, much faster!

## Slide 9: Results: MADNG vs PTC for RDT tracking
Calculating RDTs for all BPMs in the LHC is needed:
  MADX-PTC execution time: 1630.12 [s] = 27.17 [min]
  MADNG execution time: 20.00 [s] 82 times faster!
MADNG Opens new possibilities to use computationally expensive methods such as ML for non linear optics
For testing purposes a cost function is defined as the RMS of the deviation from nominal for all LHC
Fig 3. Nominal RDTs MADNG vs PTC

## Slide 10: Results: MADNG vs PTC for RDT tracking
 | RMS | RMS | RMS | RMS
Nominal | 0 | 0 | 42.87036738 | 42.87037055
in MQXA.3L2 | 1.4170 % | 1.4197 % | 43.46449129 | 43.46564095
WISE Errors in triplets | 0.469297 % | 0.469374 % | 43.07155673 | 43.07159292
Tab 1. Example cost function comparison
Differences between scripts ranging between more than enough for ML

## Slide 11: Results: Simple Bayesian Optimization for sextupolar errors in the LHC
Trivial unrealistic example, proof of concept
Trying to correct MQXA.3L2 triplet using MCSX.3L2
Convergence in 6 iterations
RMS =1.417 %
RMS =0.147% kcsx3_l2= -0.00979
Planning on optimizing multiple RDTs at once
Fig 4. Bayesian optimization results for ten iterations

## Slide 12: Conclusions and Future Improvements
Experience as a new user in MADNG vs MADX:
  Since MADNG is still in development it has a steep learning curve as of today
  However since MADNG is based in LuaJIT this allows for more flexibility than MADX
  Using MADX-PTC a ML application for RDT optimization is not feasible, MADNG proves to be a very powerful tool, and much faster
ML For RDT optimization:
  Further testing must be done to see how useful Bayesian optimization might be, more error types, more correctors…
  After finally setting up the error generation section the ML part can be explored more in depth, using BO or more classical ML
ML For tune signal denoising (autoencoders):
  In progress..

## Slide 13: References
[1] Fig 1. Bayesian optimization. By AnotherSamWilson - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=84842869
[2] Fig 1. Data pipeline. "Supervised learning-based reconstruction of magnet errors in circular accelerators" by E. Fol, 2021, https://doi.org/10.1140/epjp/s13360-021-01348-5

## Slide 14: Backup slides: Bayesian Optimization
The Bayesian optimization procedure is as follows. For t=1,2,… repeat:
  Find the next sampling point by optimizing the acquisition function over the Gaussian Process
  Obtain a possibly noisy sample from the objective function
  Add the sample to previous samples and update the surrogate function

## Slide 15: Backup slides
  trkrdt Method in MADNG 0.9.7-pre is a much faster method than cycling

## Slide 16: Backup slides